## Slide 1: GPS Security in the Military
Past, Present, and Future

## Slide 2: Some Background
the C/A code
the P(Y) code
red key and black key cryptography

## Slide 3: C/A (Coarse Acquisition) Code
1023 chips (PRN code)
repeats every millisecond
used to be degraded by SA (Selective Availability) but now is subject to “spoofing”
is modulated (along with timing, ephemeris, and other almanac data – and the P(Y) code) onto the L1 frequency (1575.42 MHz)
carries a handover word (HOW) that aids in acquiring the P(Y) code

## Slide 4
Source: http://www.sss-mag.com/pdf/Ss_jme_denayer_appl_print.pdf

## Slide 5
Source: http://pnt.gov/outreach/ieee2004/5-ImprovingTheGPSL1Signal.pdf

## Slide 6: P(Y) Code
P when unencrypted
Y when encrypted
exists on both the L1 and L2 frequencies
the PRN repeats every week

## Slide 7: Symmetric and Asymmetric Cryptography
symmetric cryptography requires the (single) “red” key to be kept secret
asymmetric cryptography has one “black” key for encryption and another for decryption – only the decryption key need be kept secret
uses the RSA algorithm

## Slide 8: The Past — PPS-SM (Precise Positioning Service Security Module)
Features | Problem
red crypto-key, changed weekly or yearly | a distribution nightmare
used the C/A code on L1 and a handover word (HOW) to acquire P(Y) on L1 and L2 | military missions might require the jamming of L1

## Slide 9: The Solution: SAASM (Selective Availability Anti-Spoofing Module)
acquires the P(Y) code directly without the C/A code
receivers equipped with SAASM must go through a rigorous security system during production
implements both symmetric and asymmetric cryptography

## Slide 10
Source: SAASM and Direct P(Y) Signal Acquisition, GPS World, July 2002

## Slide 11
Source: SAASM and Direct P(Y) Signal Acquisition, GPS World, July 2002

## Slide 12
Source: SAASM and Direct P(Y) Signal Acquisition, GPS World, July 2002

## Slide 13: The Future – The M-code and Satellite Types IIR-M II-F
IIR-M and II-F are basically equivalent in terms of military security
both will utilize the new M-code
will broadcast at a higher power level

## Slide 14: Conclusion
as with all cryptography today, the security of GPS will only be compromised by human error or deliberate giving of information
the steps being taken try to reduce as much as possible the consequences of information leaking out

## Slide 15: Partial Bibliography
GPS World
National Defense Magazine
GPS SPS Signal Specification, 2nd Edition (June 2, 1995) - (http://www.navcen.uscg.gov/pubs/gps/sigspec/default.htm)
Overview of the GPS M Code Signal - (http://www.mitre.org/work/tech_papers/tech_papers_00/betz_overview/betz_overview.pdf)